## Slide 1
ORACLE
On-desk Responsive AI Companion with Local Environment
An Embedded AI Voice Assistant for the Desktop
Faizan Ali | FA22-BCE-002
Shallum Safdar | FA22-BCE-008
Abdullah Laeeq | FA22-BCE-026
Aliyan Ahmed Cheema | FA22-BCE-028
Bachelor of Computer Engineering
Department of Computer Engineering
COMSATS University | May 2026

## Slide 2
Abstract
Hardware Platform
ESP32-WROOM32 microcontroller integrating INMP441 MEMS I2S microphone, 128×64 SSD1306 OLED, PAM8403 Class-D audio amplifier, and a push-to-talk button in a single self-contained enclosure.
Communication Pipeline
Wi-Fi WebSocket protocol connecting to a Python cloud server that orchestrates Google Gemini API calls for STT, LLM inference, and TTS synthesis.
Key Performance
Average end-to-end latency of ~3.8 seconds. Deep-sleep power management enabling over 8 hours of battery life on a 2000 mAh LiPo cell.
Audio Pipeline
Records 16-bit PCM at 16 kHz, transmits binary audio to server, receives JSON text + streamed audio reply, renders on OLED, and plays TTS through built-in DAC.

## Slide 3
Motivation & Problem Statement
01
Desk-Scale Utility Gap
No affordable, open-source desk gadget provides LLM-powered Q&A with ambient display in a single compact form factor.
02
Attention Economy
Every context switch to a phone or browser costs cognitive overhead. A dedicated single-purpose device minimises this cost.
03
Hardware Learning
Building ORACLE exposes the team to the full embedded stack demanding VLSI-level thinking about power, signal integrity, and timing.
Problem: No low-cost, open-hardware desk gadget accepts voice queries, returns LLM answers with web-search grounding, displays on OLED, vocalises via neural TTS, and runs on a rechargeable battery — without a dedicated NPU or full Linux OS.

## Slide 4
Proposed Solution — Core Components
Component | Model / Spec | Role
ESP32-WROOM32 | 240 MHz, 520 KB SRAM | Main MCU; firmware, Wi-Fi, audio
MEMS Microphone | INMP441 (I2S) | Captures 16 kHz mono PCM audio
OLED Display | SSD1306 128×64 I2C | Renders text responses & status
Audio Amplifier | PAM8403 Class-D | Drives 1W speaker from DAC
Power Supply | LiPo 2000 mAh + TP4056 | Rechargeable with USB-C charging
Push-to-Talk | Tactile switch GPIO34 | Initiates recording, avoids false triggers
Wake Sensor | KY-037 GPIO35 | Sound-triggered deep-sleep wakeup
Cloud Server | Python + WebSocket | STT / LLM / TTS via Gemini API

## Slide 5
System Architecture
Hardware Layer
INMP441 I2S Mic → ESP32-WROOM32
PAM8403 + Speaker (audio out)
SSD1306 OLED via I2C @400 kHz
KY-037 wake sensor + PTT button
LiPo + TP4056 USB-C charger
→
Transport Layer
ESP32 Wi-Fi STA mode
WebSocket Binary Protocol
Custom framing: 0xAA 0x55 header
mDNS zero-conf discovery
TCP keep-alive heartbeat
→
Cloud Layer
Python asyncio WebSocket Server
Gemini 2.5 Flash — STT + LLM
Gemini 2.5 Pro — Neural TTS
24→16 kHz polyphase resample
Google Search grounding
Pipeline: Wake/PTT → Record PCM → WebSocket Stream → STT → LLM → TTS → OLED + Speaker → Idle/Sleep

## Slide 6
Goals & Objectives
Goals
G1. Design compact hardware prototype (MCU + mic + display + speaker)
G2. Implement voice-to-LLM-to-audio pipeline via WebSocket
G3. Integrate real-time weather via IP geolocation (no GPS)
G4. Achieve end-to-end latency < 5 seconds on broadband
G5. Battery life > 4 hours active on 2000 mAh LiPo
G6. Apply VLSI principles: CMOS, PUN/PDN, FSM, timing
Key Objectives
Interface INMP441 I2S mic for 16-bit, 16 kHz PCM
Custom WebSocket binary framing (0xAA 0x55 header)
Gemini STT — English + Roman Urdu bilingual
Gemini LLM with Google Search grounding
Resample TTS 24→16 kHz, stream to I2S DAC
5-state firmware FSM with deep-sleep management
CMOS inverter sizing, I2S timing, PUN/PDN analysis

## Slide 7
Complex Engineering Problem (CEP) Analysis
Washington Accord WA2 — All 9 Attributes Addressed
WA2.1
Problem Complexity
Multi-discipline: digital hardware, analog signal integrity, real-time firmware, cloud AI, and UX design.
WA2.2
Depth of Knowledge
VLSI, embedded systems, signal processing, networking, cloud APIs, and power electronics.
WA2.3
Conflicting Requirements
Low latency vs. quality, battery life vs. always-on, privacy vs. convenience — all resolved with deliberate trade-offs.
WA2.4
Engineering Computation
Audio buffer sizing, polyphase resampling ratios, battery life, CMOS inverter sizing, I2S timing margins.
WA2.5
Tools & Technologies
ESP32, Arduino IDE, Python asyncio, Logic Analyser, LTspice, Microwind, Gemini API, WebSocket.
WA2.6
Hardware-Software-User
Custom wiring, 3-layer firmware, PTT UX validated over VAD, OLED state-machine feedback.
WA2.7
Society & Sustainability
Under $35 democratises AI; PTT ensures privacy; deep-sleep cuts idle power by 95%.
WA2.8
Novel Integration
First known combination of real-time WebSocket audio streaming + multi-model Gemini + deep-sleep ESP32.
WA2.9
UN SDGs Addressed
SDG 7 (clean energy efficiency), SDG 9 (affordable AI infra), SDG 11 (inclusive design).

## Slide 8
Engineering Calculations
Audio Buffer
fs = 16,000 Hz, bit depth = 16 bits
Chunk = 256 samples → 512 bytes
Chunk duration = 16 ms
5-sec recording ≈ 156 KB raw PCM
Resampling
TTS output: 24,000 Hz
DAC target: 16,000 Hz
GCD = 8000 → up=2, down=3
Kaiser-windowed FIR anti-alias
Battery Life
C = 2000 mAh, η = 0.85
I_active = 210 mA → 8.1 h
I_sleep = 12 µA → 142,000 h
Mixed-use ≈ 15.3 h
CMOS Inverter
(W/L)p / (W/L)n = 2.5
If (W/L)n = 2, (W/L)p = 5
t_p ≈ 200 ps at 10 fF load
BCLK period 977 ns >> 200 ps ✓

## Slide 9
Performance Results
Metric | Target | Measured | Status
STT Latency (5 s clip) | ≤ 1.5 s | 0.8 – 1.2 s | ✓ PASS
LLM Inference Latency | ≤ 2.0 s | 1.0 – 1.8 s | ✓ PASS
TTS Synthesis Latency | ≤ 1.5 s | 0.8 – 1.2 s | ✓ PASS
Total Round-Trip | ≤ 5.0 s | 3.5 – 4.8 s | ✓ PASS
Active Power Draw | ≤ 300 mA | 205 – 215 mA | ✓ PASS
Deep-Sleep Current | ≤ 100 µA | ~12 µA | ✓ PASS
Battery Life (Active) | ≥ 4 hours | ~8.1 hours | ✓ PASS
STT Accuracy (English) | ≥ 90% | ~95% | ✓ PASS
STT Accuracy (Roman Urdu) | ≥ 80% | ~82% | ✓ PASS

## Slide 10
Advantages & Limitations
Advantages
Minimal BOM — under $35 total component cost
No dedicated NPU — AI fully cloud-offloaded
Upgradeable LLM/TTS by server config change only
Privacy-first: PTT — no continuous audio streaming
Bilingual STT — English + Roman Urdu
12 µA deep-sleep → months of standby battery
Fully open-source firmware + server
Limitations
Requires active Wi-Fi — no offline operation
Recurring Gemini API costs at sustained use
128×64 OLED limits visible text per screen
Single mic — degrades above ~65 dB ambient noise
IP geolocation ±30 km accuracy only
API latency spikes can breach 5-second target
No multi-turn conversation memory per session

## Slide 11
Applications
1
Student Productivity
Instant academic Q&A without leaving the study desk
2
Developer Workstation
Voice lookup of API docs, code explanations, commands
3
Ambient Info Hub
Continuous weather, time & data display on desk or shelf
4
Accessibility Aid
Hands-free information for users with motor impairments
5
Language Learning
Conversational AI practice + pronunciation feedback
6
Smart Office
Meeting reminders, task readouts, quick calculations
7
Education Platform
Tangible teaching tool for embedded AI & VLSI courses

## Slide 12
Future Scope & Recommendations
Hardware
2-layer PCB with dedicated audio/digital ground planes
3-mic INMP441 array with beamforming firmware
BME280 for local room temperature & humidity
MAX98357A I2S digital amplifier to eliminate DAC noise
Firmware / Software
Multi-turn conversation with 4-exchange sliding window
ESP-SR local wake-word on ESP32-S3 (hands-free)
AES-128 WebSocket audio encryption
OTA firmware update mechanism
AI & Cloud
Evaluate Anthropic Claude Haiku / OpenAI GPT-4o-mini
Response caching for time & weather queries
Local llama.cpp fallback on Raspberry Pi Zero 2W
Multi-device ORACLE mesh via MQTT broker

## Slide 13
Conclusion
~3.8s
End-to-End Latency
8.1h
Active Battery Life
12µA
Deep-Sleep Current
<$35
Total Component Cost
ORACLE proves that a fully-functional LLM-powered voice assistant can run on a $15 ESP32 with under $35 in components. All primary performance targets were met. The project reinforces core VLSI concepts — CMOS drivers, PUN/PDN logic, FSM design, I2S timing, and power estimation — while mapping cleanly to all 9 Washington Accord WA2 Complex Engineering Problem attributes.
The system is fully open-source and replicable by any team with an ESP32 dev kit, a Python server, and a Google AI Studio API key — demonstrating that frontier AI fits in the palm of your hand.
Department of Computer Engineering | COMSATS University | May 2026